Yaesu FT Dx-9000

TECHNICAL LIBRARY

Frequency band jumper selection document

Maximo – EA1DDO / HK1DX

www.EA1DDO.es

mailto:ea1ddo@hotmail.com

| TECHNICAL LIBRARY |
| --- |
| MODEL: FT DX 9000 series |
| File No. | TL_FTDX9000.doc | Serial Number range | ALL |
| Date of issue: | 2026.01.06 | Page | 2 |
|  | Maximo - EA1DDO / HK1DX | www.EA1DDO.es |
| Type | Frequency Band | Jumper |
|  | 1.8 Mhz | 3.5 Mhz | 5 Mhz | 7 Mhz | 10 Mhz | 14 Mhz | 18 Mhz | 21 Mhz | 24 Mhz | 28 Mhz | 50 Mhz | JP5001 | JP5003 | JP5005 |
| EU/ FRG | 1.815000- 1.889999 | 3.500000- 3.799999 |  | 7.000000- 7.099999 | 10.100000- 10.149999 | 14.000000- 14.349999 | 18.068000- 18.167999 | 21.000000- 21.449999 | 24.890000- 24.989999 | 28.000000- 28.699999 | 50.080000- 50.399999 |  | O | O |
| FRA | 1.810000- 1.849999 | ↑ |  | ↑ | ↑ | ↑ | ↑ | ↑ | ↑ | ↑ | 50.200000- 51.199999 | O |  |  |
| UK | 1.810000- 1.999999 | ↑ | 5.260000, 5.280000, 5.290000, 5.400000, 5.405000 | 7.000000- 7.199999 | ↑ | ↑ | ↑ | ↑ | ↑ | ↑ | 50.000000- 51.999999 |  | O |  |
| EXP/ AUS | 1.800000- 1.999999 | 3.500000- 3.999999 |  | 7.000000- 7.299999 | ↑ | ↑ | ↑ | ↑ | ↑ | ↑ | 50.000000- 53.999999 | O | O |  |
| USA | ↑ | ↑ | 5.167500, 5.332000, 5.3480000, 5.3680000, 5.3730000, 5.4050000 | ↑ | ↑ | ↑ | ↑ | ↑ | ↑ | ↑ | ↑ |  |  |  |
| JPN | 1.810000- 1.824999, 1.907500- 1.912499 | 3.500000- 3.574999, 3.747000- 3.753999, 3.791000- 3.804999 | 4.630.000 | 7.000000- 7.099999 | ↑ | ↑ | ↑ | ↑ | ↑ | ↑ | ↑ |  |  | O |
| Mars | Tx 1.8 - 30 Mhz & 50 - 54 Mhz | JP5007 & JP5011 only |

Then all reset, power on while pushing ¨Fast¨ key and ¨Lock¨ key at the same time.